## Slide 1: Touch Free Facemask and Temperature Station

## Slide 2: Current Stations

## Slide 3: MODEL DESIGN
1
IMAGE RECOGNITION
TinyML (TFLite) KERAS OPENCV DLIB
SOFTWARE
RaspPi OS (Raspbian) PyCharm Thonny IDE
HARDWARE
Raspberry Pi 3 B+ RPi Camera V1 MLX90614 IR Sensor Nextion 5” TFT Display
INTERFACE
FLASK DASH

## Slide 4: HARDWARE AND DRIVERS
MLX90614 IR Thermometer
SMBus & I2C (SDA & SLC)
5” TFT Display
RX TX serial bus
RPi Cam V1 (1 MP)
CSI Bus

## Slide 5: MODEL DESIGN
Restrictions:
1GB RAM (800MHz LPDDR2)
Embedded GPU ( No dedicated GDDR memory)
1.2 GHz ARM Cortex quad core (A53)
Model | Pros | Cons
OpenCV Haar | CPU processing | Low Accuracy
OpenCV DNN | High Accuracy | High RAM Usage
Dlib HOG | Lightweight | Requires good lighting

## Slide 6: APPLICATION Local Host: Flask Live Feed: Dash Imagery Overlay: openCV

## Slide 7: COMPONENTS AND COST
AMAZON
ALIEXPRESS

## Slide 8: IMPROVEMENTS
Specialized Microcontroller
HD 10mp+ Camera
Non SMBus Sensor
Automatic Calibration
Data Logging

## Slide 9: THANKS! Any questions?
Project GitHub repo:
git@github.com:RamonMartin1/tmpst.git
Email for additional info at:
martin.ramon.f@gmail.com